Hot Air Lance

Operation Manual

PARTS CHECK LIST

NOTE:  Check all fittings & connections prior to operation.

    - A:  Heat Lance

    - B:   Red propane regulator

    - C:  Regulator Gauge

    - D:   Hose Kit Assembly

    - E:   Air Coupler Q/D

    - F:   Propane Plug Q/D

    - G:   Black Water Seperator

    - H:  Compressor Fitting

    - I:  Wheel Kit (Optional)

    - J:   Shoulder Strap

Hot Air Lance Assembly Instructions

To Assemble Your Unit

Remove stop nut from regulator with socket wrench, heat may be needed to loosen nut. Insert regulator gauge in opening & tighten.





Attach female end of propane hose (smaller hose)to red gas regulator fitting & tighten. This is a left hand thread.



3.	Attach air hose to the outlet side of the water separator (towards arrow) and tighten.

Insert compressor tank fitting to inlet side (away from arrow) of separator and tighten. Always use clip with fitting when in use.

Insert lance burner head into opening on wheel kit. Push unit all the way into opening and tighten bolts to hold unit in place.





If you have any problems with your assembly, please contact your local heat lance representative

Start Up & Operation

REMEMBER SAFETY FIRST

WARNING    Due to the heat & noise of the hot air lance, eye and hearing protection are advised. Boots, gloves and protective gear should be worn during operation of unit Always check to be sure that all persons operating this equipment have read these instructions and are familiar with its operation and potential hazards. This unit can cause severe burns if used improperly. Burner tube will remain very hot after operation and should not be touched until it has had plenty of time to cool down.

This unit requires a minimum of at least 3/8” air supply hose with bore fittings and no more than 60’ in length. Any additional distance requirements can be met by using a ¾” air hose at compressor end. The air filter supplied with the unit must remain in an upright position to function properly.

When in operation, the unit is maintaining very high temperatures and extreme caution should be used. The unit must not be used near edges of buildings or near dry grassy areas. If so use extreme caution. LA*B takes no responsibility for

misuse or improper operation. The lance must not be left unattended or left running and must not be set down or placed on flammable materials until it has cooled down.

Operation

- Make air and LP connections at lance handle. Insure all fittings and connections are tight. If leaks are detected Do Not Operate Unit. Tighten as needed and start over.

- To light unit, first make sure no flammable materials are present in working area. When working with LP Gas always light the lance facing downwind. Be sure all operators have fully read this manual and are knowledgeable on its operation and safety hazards.

- Set regulator to 15 – 25 psi on gauge (If visible flame is present during operation LP psi is set too high. No flame should be visible)

- Close both ball valves on lance. Both valves should be in vertical positions.

- Start air compressor

- Open air line on compressor.

- Open top and bottom ball valve slightly (combustion valves) slightly to allow small amount of air flow through unit.

8.  Close LP Needle valve on lance.

9. Open LP Tank valve

10. Open LP needle valve ¼ turn

11 . Using a long neck lighter, light lance in ignition holes atop of burner tube. Never attempt to light lance at burner tube base as severe burns could result if LP Gas valve is too far open.

12.  Slowly open needle valve and top ball valve together. (Be sure to open LP needle valve at a faster rate than air valve or unit will extinguish. If this occurs close all valves and start over.) Once top ball valve is half way open, open bottom ball valve 100%.

13. Continue to open top ball valve and LP needle valve until top ball valve is wide open.

14.  Slowly cut back the LP needle valve until lance produces a jet engine roaring sound and the flame is pulled back into the burner chamber. There should be no visible flame during operation. If there is a visible flame adjust LP settings at this time.

15.  To adjust the BTU downward, first slowly close down some air to the combustion system using the top ball valve. Then turn down the propane needle valve until the combustion is at its optimum mixture. No flame should be present at that time. Alternate between the air & propane settings in small steps until the desired setting is reached.

Shut Down Procedure

A: 	Turn off propane supply by needle valve and propane tank.

	   

Allow air to flow through burner chamber and the air lance tube until they have cooled down.

After unit(s) have had sufficient time to cool, shut down propane line and compressor line at main units.

Disconnect hoses by way of fittings at lance handle.



Hot Air Lance Safety Checklist:

The hot air lance operates at very high temperatures. Always use common sense while operating the unit.

The lance produces high velocity hot air. Never point the lance above the waist or at another person when operating the unit

Never touch the burner tube when or after use as severe burns will result.

Always allow the unit to thoroughly cool before loading into truck or handling the unit.

When lighting the unit always point lance downwind

Never light unit near flammable materials

Always check fittings and connections prior to use.

Prior to each use, check hoses for cuts or leaks.

Do not operate unit near or around wooden structures or baseboards

Always wear eye, hand and hearing protection during operation.

All operators of the unit should be familiar with its safety precautions and potential injuries during use.

If you have any questions or concerns please feel free to contact us at 800-776-5830

LA*B Manufacturing     800-776-5830    Cincinnati, OH 45215